## Slide 1: IP Addresses
Notes: 1

## Slide 2: IP Addresses
An identifier for a computer or device on a TCP/IP network. Networks using the TCP/IP protocol route messages based on the IP address of the destination. The format of an IP address is a 32-bit numeric address written as four numbers separated by periods. Each number can be zero to 255. For example, 1.160.10.240 could be an IP address.

## Slide 3: IP Address Classes
Class A - 168.212.226.204
supports 16 million hosts on each of 127 networks
Class B - 168.212.226.204
supports 65,000 hosts on each of 16,000 networks
  NDUS has two Class B addresses
    134.129.xxx.xxx Eastern ND
    134.234.xxx.xxx Western ND
Class C - 168.212.226.204
supports 254 hosts on each of 2 million networks

## Slide 4: IPv4 vs. IPv6
IPv4
  32 bits used for address
  4,294,967,296
  Addresses not assigned by geographic region (see map)
IPv6
  128 bits used for address
  340,282,366,920,938,463,374,607,431,768,211,456
  That about 3.7x10^21 addresses per square inch of the earth’s surface
  Addresses will be assigned by geographic region

## Slide 5: IPv4 vs. IPv6
IPv4 addresses written as four octets (8 bits) separated by periods.
  134.129.67.235
IPv6 address written as eight 4-digit (16-bit) hexadecimal numbers separated by colons.
  1080:0:0:0:0:800:0:417A

## Slide 6: IPv4-to-IPv6
IPv4 Compatible Address
  0:0:0:0:0:0:w.x.y.z (or ::w.x.y.z)
  Is used by dual-stack nodes that are communicating with IPv6 over an IPv4 infrastructure
  The last four octets (w.x.y.z) represent the dotted decimal representation of an IPv4 address

## Slide 7: Loopback address
127.0.0.0
  Network number that cannot be assigned to any network
127.0.0.1
  The loopback address
  Used for diagnostic testing of the local TCP/IP installation

## Slide 8: Automatic Private IP Addressing (APIPA)
169.254.x.x
IP addresses are self-assigned when the computer asks for an IP address and no one responds.
i.e. the computer cannot reach a DHCP server over the network.

## Slide 9: Network & Broadcast addresses
You cannot assign a network number to a computer or any other host on the network.
You cannot assign the highest number on a network to a host. This address is interpreted as a broadcast message for the subnet.

## Slide 10: Reserved IP Network Numbers
Network number | Subnet mask | IP address range
10.0.0.0 | 255.0.0.0 | 10.0.0.1-10.255.255.255
172.16.0.0-172.31.0.0 | 255.255.0.0 | 172.16.0.1-172.31.255.255
192.168.0.0 | 255.255.255.0 | 192.168.0.1-192.168.255.255
Designed for use on a private network behind a Network Address Translation (NAT) device, such as a firewall, proxy servers, or some routers. A NAT device can be used to disguise local or internal IP addresses from outside networks. For more reserved addresses see: http://en.wikipedia.org/wiki/Reserved_IP_addresses |  | 

## Slide 11: Uniform Resource Locator
http://www.ndsu.nodak.edu/pubweb/~latimer/index.html#events
http:// communication protocol
www.ndsu.nodak.edu web server hosting the page
/ndsu/latimer/ path to the page on the host server
index.html filename of the page
#events anchor in the page

## Slide 12: IP & Domain Name Examples
IP: 134.129.67.85
URL: gdc.busad.ndsu.nodak.edu
IP: 134.129.67.235
URL: dyn235.minard-67.ndsu.nodak.edu

## Slide 13: ICANN
Internet Corporation for Assigned Names and Numbers
a private sector, nonprofit organization
responsibility for IP address space allocation, protocol parameter assignment, domain name system management and root server system management functions previously performed under U.S. Government contract
ICANN's diverse board consists of nineteen Directors, nine At-Large Directors, who serve one-year terms and will be succeeded by At-Large Directors elected by an at-large membership organization. None of the present interim directors may sit on the board once the permanent members are selected.

## Slide 14: IP Address Registries
Regional Internet Registries:
American Registry for Internet Numbers, ARIN
Réseaux IP Européens Network Coordination Centre, RIPE NCC
Asia Pacific Network Information Centre, APNIC
Latin American and Caribbean Internet Addresses Registry, LACNIC

## Slide 15: Internet Assigned Numbers Authority http://www.iana.org/
Generic Top-Level Domains
  http://www.iana.org/gtld/gtld.htm
ccTLD Database (country codes)
  http://www.iana.org/cctld/cctld-whois.htm
IP Address Services
  http://www.iana.org/ipaddress/ip-addresses.htm

## Slide 16: New Top-Level Domain Names (TLDs)
ICANN is accepting applications for new TLDs.
  Application window Jan. 12, 2012 to Apr. 12, 2012
  Application fee: $185,000
  Annual fee: $25,000
Intent is to move towards more descriptive names
Companies (organizations) can create
  Brand domains e.g. .pepsi .coke
  Generic domains e.g. .car .green
http://mashable.com/2011/06/20/icann-top-level-domains/